Instructions for Using Profile Equations

The methodology for calculating class hourly profile kW values was developed by running regression models on class historical demand data as a function of hourly temperature values.  The models produced temperature breakpoint ranges, along with equations and its associated coefficients and constants that will be applied in the calculation of the class profile kW.  Regarding breakpoint ranges, the Load Profile Process detects changes in inflection points in the hourly data (based on confidence band, co-efficient of correlation, t-statistic), prompting a breakpoint at certain data points where necessary.  The write up below provides an explanation of how the regression models are used in the profile calculations along with some examples.  The profile values are calculated at the sales level.  Profile values at generations level = Sales Level Profile Value*loss factor.

The profile equations are generated using a 4 season adjusted, 2 day-type model.  The following defined adjusted seasons correspond to the following stated time periods:

Winter: 	December 1st  to March 18th

Spring: 	March 19th  to May 24th

Summer: 	May 25th to September 10th

Fall:		September 11th to November 30th

The equations in general form:

Let … = coefficients associated with temperature ranges 1 through n.

= Regression constant.

= Temperature value for given hour (ending).

= Calculated profile value at sales level.

… = upper limit for each temperature range

Ex 1: GS1, SPRING WEEKDAY HOUR 14, TEMP=50 DEGREES F:

| HIGH_1 | HIGH_2 | HIGH_3 | HIGH_4 | COEFF_1 | COEFF_2 | COEFF_3 | COEFF_4 | CONSTANT |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 50.4741 | 64.5280 | 77.3043 | 99999 | -0.0204 | -0.0028 | 0.0055 | 0.0297 | 2.5810 |

Temp is 50 degrees FAHR which is in range 1 (0-50.4741).  Use equation:

= Profile Value for range 1

= COEFF_1 = -0.0204

= TEMP = 50

= CONSTANT = 2.581

= -0.02037 (50) + 2.581

=1.5625

Ex 2: GS1, SPRING WEEKDAY HOUR 14, TEMP=60 DEGREES F:

| HIGH_1 | HIGH_2 | HIGH_3 | HIGH_4 | COEFF_1 | COEFF_2 | COEFF_3 | COEFF_4 | CONSTANT |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 50.4741 | 64.5280 | 77.3043 | 99999 | -0.0204 | -0.0028 | 0.0055 | 0.0297 | 2.5810 |

Temp is 60 degrees FAHR which is in range 2 (50.4741-64.5280).  Use equation:

= Profile Value for range 2

= COEFF_1 = -0.0204

= COEFF_2 = -0.0028

= TEMP = 60

= CONSTANT = 2.581

= HIGH_1 = 50.4741

= -0.0204(50.4741) + -0.0028(60-50.4741) + 2.5810

=1.5343

Ex 3: GS1, SPRING WEEKDAY HOUR 14, TEMP=70 DEGREES F:

| HIGH_1 | HIGH_2 | HIGH_3 | HIGH_4 | COEFF_1 | COEFF_2 | COEFF_3 | COEFF_4 | CONSTANT |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 50.4741 | 64.5280 | 77.3043 | 99999 | -0.0204 | -0.0028 | 0.0055 | 0.0297 | 2.5810 |

Temp is 70 degrees FAHR which is in range 3 (64.5280-77.3043).  Use equation:

= Profile Value for range 3

= COEFF_1 = -0.0204

= COEFF_2 = -0.0028

= COEFF_3 = 0.0055

= TEMP = 70

= CONSTANT = 2.581

= HIGH_1 = 50.4741

= HIGH_2 = 64.528

= -0.0204(50.4741) + -0.0028(64.528-50.4741) + 0.0055(70-64.528) + 2.581

=1.5419

Ex 4: GS1, SPRING WEEKDAY HOUR 14, TEMP=80 DEGREES F:

| HIGH_1 | HIGH_2 | HIGH_3 | HIGH_4 | COEFF_1 | COEFF_2 | COEFF_3 | COEFF_4 | CONSTANT |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 50.4741 | 64.5280 | 77.3043 | 99999 | -0.0204 | -0.0028 | 0.0055 | 0.0297 | 2.5810 |

Temp is 80 degrees FAHR which is in range 4 (77.3043-99999).  Use equation:

= Profile Value for range 4

= COEFF_1 = -0.0204

= COEFF_2 = -0.0028

= COEFF_3 = 0.0055

= COEFF_4 = 0.0297

= TEMP = 80

= CONSTANT = 2.581

= HIGH_1 = 50.4741

= HIGH_2 = 64.528

= HIGH_3 = 77.3043

= -0.0204(50.474) + -0.0028(64.528-50.4741) + 0.0055(77.3043-64.528) + 0.0297(80-77.3043) + 2.581

=1.6622

# Text boxes

If temp falls in 1st range.

If temp falls in nth range.

If temp falls in 3rd range.

If temp falls in 2nd range.